## Slide 1
第 1 章 Chapter 1
CMOS 反相器
The CMOS Inverter
从一个晶体管开关出发，理解数字芯片的电平、速度与功耗
From one transistor switch to the levels, speed and power of digital chips
数字集成电路设计 Digital Integrated Circuit Design · 问渠 WenQuest
Notes: 开场问题：机器人关节里的电机控制芯片，最基本的单元是什么？它的电平、速度、功耗由什么决定？ Opening question: what is the most basic cell in a robot joint’s motor-control chip, and what sets its levels, speed and power?

## Slide 2
本章内容与每节课的结构
Chapter map and how each lesson works
1.1
MOSFET 开关与 CMOS 反相器
MOSFET switches and the CMOS inverter
机器人问题：关节驱动板的光耦输入
Robot: Optocoupler input on a joint driver
1.2
电压传输特性与噪声容限
Voltage transfer characteristic and noise margins
机器人问题：编码器信号的抗干扰
Robot: Noise immunity of an encoder signal
1.3
尺寸与对称
Sizing and symmetry
机器人问题：电机控制芯片的时钟缓冲
Robot: The clock buffer of a motor-control chip
1.4
传播延时与反相器链
Propagation delay and the inverter chain
机器人问题：驱动板上的栅极驱动器
Robot: Driving the gate driver on the board
1.5
功耗
Power
机器人问题：巡线小车控制芯片的功耗预算
Robot: Power budget of a line-following car controller
每节课：实际问题 → 概念 → 动画 → 虚拟实验 → 建模求解 Each lesson: problem → concept → animation → virtual lab → modelling
Notes: 芯片设计同样靠模型：先用简单模型估算，再用仿真和工艺库校准。本章每节从一个机器人问题出发，最后回到这个问题。 Chip design also runs on models: estimate with a simple model, then calibrate with simulation and the process library. Each lesson starts from a robot problem and returns to it.

## Slide 3
1.1 机器人问题 Robot problem
关节驱动板的光耦输入
Optocoupler input on a joint driver
关节驱动板用光耦隔离控制芯片与功率电路。芯片输出管脚要吸收 1 mA 点亮光耦，低电平不能超过 0.2 V。输出级的 NMOS 至少要多宽？
The joint driver isolates the control chip from the power stage with an optocoupler. The output pin must sink 1 mA with a low level of at most 0.2 V. How wide must the output NMOS be?
已知 Given
负载电流 I = 1 mA
load current I = 1 mA
VOL ≤ 0.2 V，VDD = 1.8 V
VOL ≤ 0.2 V, VDD = 1.8 V
L = 0.15 μm，k′n = 90 μA/V²（示意值）
L = 0.15 μm, k′n = 90 μA/V² (illustrative)
本节结束时，我们用建立的模型回答这个问题。 We will answer it with this lesson’s model at the end.
Notes: 先让学生估一估、讨论 2 分钟，不急于给答案。本节最后回到这一页。 Let students estimate and discuss for two minutes; return to this problem at the end.

## Slide 4
1.1 概念 Concept
开关模型与互补结构
Switch model and complementary structure
MOSFET 是电压控制的开关：VGS > VT 导通，VGS < VT 截止
A MOSFET is a voltage-controlled switch: on for VGS > VT, off below
CMOS 反相器：PMOS 上拉、NMOS 下拉，栅极接在一起
CMOS inverter: PMOS pull-up, NMOS pull-down, gates tied together
稳态时总有一个管子截止：没有静态直流通路
One transistor is always off in steady state: no static DC path
导通的管子工作在线性区，相当于电阻 Ron
The on transistor sits in the linear region and acts as a resistor Ron
线性区 ID = k′n(W/L)[(VGS−VT)VDS − VDS²/2]
Ron ≈ 1 / [k′n(W/L)(VDD − VT)]
Notes: 讲清公式中每个量的意义和模型的适用条件，再进入动画。 Explain each quantity and the model’s conditions before the animation.

## Slide 5
1.1 动画 Animation
输入从 0 变到 1，电流走哪条路？稳态时还有电流吗？
When the input goes from 0 to 1, where does the current flow? Is there any current in steady state?
点击画面播放 · 中英字幕 · Click to play · bilingual captions
Notes: 播放动画，在关键画面暂停提问。 Play the clip and pause at the key frame to ask the question on the slide.

## Slide 6
1.1 虚拟实验 Virtual lab
动手试一试：MOSFET 开关与 CMOS 反相器
Try it: MOSFET switches and the CMOS inverter
任务 Tasks
切换输入高低，观察哪个管子导通
Toggle the input and see which transistor conducts
光耦 1 mA：找出 VOL ≤ 0.2 V 的最小 Wn
Optocoupler 1 mA: find the smallest Wn with VOL ≤ 0.2 V
负载加到 2 mA，VOL 正好翻倍吗？
At 2 mA, does VOL exactly double?
打开虚拟实验 Open lab ▶
实验台中选“1.1”选项卡 · 课后按实验指导书完成实验报告
Choose tab 1.1 · write the lab report using the lab guide
Notes: 课堂投屏演示机器人任务，其余任务课后完成，并按实验指导书写实验报告。 Demonstrate the robot task in class; students finish the rest and the lab report after class.

## Slide 7
1.1 回到实际问题 Back to the problem
建模求解：关节驱动板的光耦输入
Modelling: Optocoupler input on a joint driver
步骤 Step | 内容 What we do
① 问题 Problem | 关节驱动板用光耦隔离控制芯片与功率电路。芯片输出管脚要吸收 1 mA 点亮光耦，低电平不能超过 0.2 V。输出级的 NMOS 至少要多宽？ The joint driver isolates the control chip from the power stage with an optocoupler. The output pin must sink 1 mA with a low level of at most 0.2 V. How wide must the output NMOS be?
② 建模 Model | 输入为高，NMOS 栅压 1.8 V，工作在线性区；平方律模型，忽略沟道长度调制 Input high, NMOS gate at 1.8 V in the linear region; square law, no channel-length modulation
③ 求解 Solve | W ≥ I·L / {k′n[(VDD−VT)VOL − VOL²/2]} = 6.67 μm（W/L ≈ 44）；2 mA 时 VOL ≈ 0.44 V，不止翻倍 W ≥ I·L / {k′n[(VDD−VT)VOL − VOL²/2]} = 6.67 μm (W/L ≈ 44); at 2 mA VOL ≈ 0.44 V, more than double
④ 检验 Check | 虚拟实验 1.1：负载 1 mA，调 Wn 读 VOL；负载线与输出特性的交点 Lab 1.1: load 1 mA, adjust Wn and read VOL where the load line meets the curve
⑤ 修正 Improve | 实际要按 SKY130 模型和温度、工艺角留余量；电流更大时改用专门的输出驱动或外接三极管 Use SKY130 models with margin for temperature and corners; for larger currents use a dedicated driver or an external transistor
生活中的例子
Everyday example
楼梯间双控开关：两个开关互补，灯只有亮、灭两种状态
Two-way stair switches are complementary: the light is either on or off
芯片设计也靠模型：先用简单模型估算，再用仿真和工艺库校准，最后指出模型的局限。
Chip design runs on models: estimate simply, calibrate with simulation and the process library, then name the limits.
Notes: 对照五步讲解，强调第⑤步：模型在哪里失效。实验报告第六部分按这五步写。数值为示意参数下的结果，以后按 SKY130 校准。 Walk through the five steps, stressing step ⑤. Section 6 of the lab report follows them. Numbers use illustrative parameters, to be calibrated to SKY130.

## Slide 8
1.2 机器人问题 Robot problem
编码器信号的抗干扰
Noise immunity of an encoder signal
关节编码器的信号经 2 m 电缆进入控制芯片，电机工作时叠加约 ±0.3 V 干扰。接收端的反相器会不会误翻转？
The joint encoder signal travels 2 m of cable into the control chip and picks up about ±0.3 V of motor noise. Will the receiving inverter switch falsely?
已知 Given
干扰幅度 ±0.3 V
noise ±0.3 V
VDD = 1.8 V，|VT| = 0.45 V
VDD = 1.8 V, |VT| = 0.45 V
迁移率比 r = k′n/k′p = 2.25
mobility ratio r = k′n/k′p = 2.25
本节结束时，我们用建立的模型回答这个问题。 We will answer it with this lesson’s model at the end.
Notes: 先让学生估一估、讨论 2 分钟，不急于给答案。本节最后回到这一页。 Let students estimate and discuss for two minutes; return to this problem at the end.

## Slide 9
1.2 概念 Concept
传输特性：阈值与噪声容限
Transfer curve: threshold and noise margins
两管电流相等决定输出电压，逐点画出 Vout(Vin)
Equal currents set Vout; plot Vout(Vin) point by point
两管都饱和处曲线最陡：开关阈值 VM
The curve is steepest where both saturate: the threshold VM
斜率为 −1 的两点定出 VIL、VIH
The two slope = −1 points define VIL and VIH
NML = VIL − VOL，NMH = VOH − VIH
NML = VIL − VOL, NMH = VOH − VIH
VM = [VTn + r′(VDD − |VTp|)] / (1 + r′)
r′ = √(k′pWp / k′nWn)
Notes: 讲清公式中每个量的意义和模型的适用条件，再进入动画。 Explain each quantity and the model’s conditions before the animation.

## Slide 10
1.2 动画 Animation
输入慢慢增大，两个管子的工作区怎样变化？曲线为什么在中间几乎竖直？
As the input rises, how do the two transistors change region? Why is the curve almost vertical in the middle?
点击画面播放 · 中英字幕 · Click to play · bilingual captions
Notes: 播放动画，在关键画面暂停提问。 Play the clip and pause at the key frame to ask the question on the slide.

## Slide 11
1.2 虚拟实验 Virtual lab
动手试一试：电压传输特性与噪声容限
Try it: Voltage transfer characteristic and noise margins
任务 Tasks
调尺寸比使 VM = 0.90 V
Adjust the ratio until VM = 0.90 V
尺寸比 1：读出 NML
Ratio 1: read NML
干扰 0.30 V：两个容限都 ≥ 0.6 V
Noise 0.30 V: both margins ≥ 0.6 V
打开虚拟实验 Open lab ▶
实验台中选“1.2”选项卡 · 课后按实验指导书完成实验报告
Choose tab 1.2 · write the lab report using the lab guide
Notes: 课堂投屏演示机器人任务，其余任务课后完成，并按实验指导书写实验报告。 Demonstrate the robot task in class; students finish the rest and the lab report after class.

## Slide 12
1.2 回到实际问题 Back to the problem
建模求解：编码器信号的抗干扰
Modelling: Noise immunity of an encoder signal
步骤 Step | 内容 What we do
① 问题 Problem | 关节编码器的信号经 2 m 电缆进入控制芯片，电机工作时叠加约 ±0.3 V 干扰。接收端的反相器会不会误翻转？ The joint encoder signal travels 2 m of cable into the control chip and picks up about ±0.3 V of motor noise. Will the receiving inverter switch falsely?
② 建模 Model | 接收端为最小反相器；干扰叠加在输入电平上；容限至少为干扰的 2 倍 The receiver is a minimum inverter; noise adds to the input level; margins should be at least twice the noise
③ 求解 Solve | Wp/Wn = 1：VM ≈ 0.81 V，NML ≈ 0.55、NMH ≈ 0.82 V；Wp/Wn = 2.25：VM = 0.90 V，NML = NMH ≈ 0.675 V Wp/Wn = 1: VM ≈ 0.81 V, NML ≈ 0.55, NMH ≈ 0.82 V; Wp/Wn = 2.25: VM = 0.90 V, NML = NMH ≈ 0.675 V
④ 检验 Check | 虚拟实验 1.2：干扰幅度设为 0.30 V，比较不同尺寸比下的两个容限 Lab 1.2: set the noise to 0.30 V and compare both margins for different ratios
⑤ 修正 Improve | 干扰更大时用施密特触发器（有回差）或差分信号（如 RS-422 编码器接口） For larger noise use a Schmitt trigger (hysteresis) or differential signalling (e.g. an RS-422 encoder interface)
生活中的例子
Everyday example
声控楼道灯的阈值：太低会被杂音触发，太高叫不亮
A sound-activated stair light: too low a threshold triggers on noise, too high won’t respond
芯片设计也靠模型：先用简单模型估算，再用仿真和工艺库校准，最后指出模型的局限。
Chip design runs on models: estimate simply, calibrate with simulation and the process library, then name the limits.
Notes: 对照五步讲解，强调第⑤步：模型在哪里失效。实验报告第六部分按这五步写。数值为示意参数下的结果，以后按 SKY130 校准。 Walk through the five steps, stressing step ⑤. Section 6 of the lab report follows them. Numbers use illustrative parameters, to be calibrated to SKY130.

## Slide 13
1.3 机器人问题 Robot problem
电机控制芯片的时钟缓冲
The clock buffer of a motor-control chip
电机控制芯片的时钟经缓冲器分发到 PWM 计数器。缓冲器上升、下降延时不同，时钟占空比就会走样。尺寸比怎样取才能让两种延时接近？
The motor-control chip distributes its clock through buffers to the PWM counter. Unequal rise and fall delays distort the duty cycle. Which size ratio matches them?
已知 Given
负载：4 个相同反相器（FO4）
load: four identical inverters (FO4)
Wn = 0.42 μm（最小）
Wn = 0.42 μm (minimum)
Req ≈ ¾·VDD/IDSAT
Req ≈ ¾·VDD/IDSAT
本节结束时，我们用建立的模型回答这个问题。 We will answer it with this lesson’s model at the end.
Notes: 先让学生估一估、讨论 2 分钟，不急于给答案。本节最后回到这一页。 Let students estimate and discuss for two minutes; return to this problem at the end.

## Slide 14
1.3 概念 Concept
RC 延时与对称尺寸
RC delay and symmetric sizing
导通管看成等效电阻 Req，负载看成电容 CL
Treat the on transistor as Req and the load as CL
tPHL = 0.69·Req,n·CL，tPLH = 0.69·Req,p·CL
tPHL = 0.69·Req,n·CL, tPLH = 0.69·Req,p·CL
PMOS 迁移率低：同尺寸时 Req,p ≈ 2.25 × Req,n
Lower PMOS mobility: at equal size Req,p ≈ 2.25 × Req,n
Wp/Wn = r：上升下降相等；Wp/Wn ≈ √r：平均延时最小
Wp/Wn = r equalises edges; Wp/Wn ≈ √r minimises average delay
tp = (tPHL + tPLH) / 2 = 0.69 · CL · (Req,n + Req,p) / 2
Notes: 讲清公式中每个量的意义和模型的适用条件，再进入动画。 Explain each quantity and the model’s conditions before the animation.

## Slide 15
1.3 动画 Animation
加宽 PMOS 以后，传输特性和输出波形各发生了什么变化？
After widening the PMOS, what changes in the transfer curve and the output waveform?
点击画面播放 · 中英字幕 · Click to play · bilingual captions
Notes: 播放动画，在关键画面暂停提问。 Play the clip and pause at the key frame to ask the question on the slide.

## Slide 16
1.3 虚拟实验 Virtual lab
动手试一试：尺寸与对称
Try it: Sizing and symmetry
任务 Tasks
FO4：使上升下降相差 ≤ 5%
FO4: make rise and fall differ by ≤ 5%
FO4：找出平均延时最小的尺寸比
FO4: find the ratio with the smallest average delay
Wp/Wn = 1 时延时差多少？
How large is the mismatch at Wp/Wn = 1?
打开虚拟实验 Open lab ▶
实验台中选“1.3”选项卡 · 课后按实验指导书完成实验报告
Choose tab 1.3 · write the lab report using the lab guide
Notes: 课堂投屏演示机器人任务，其余任务课后完成，并按实验指导书写实验报告。 Demonstrate the robot task in class; students finish the rest and the lab report after class.

## Slide 17
1.3 回到实际问题 Back to the problem
建模求解：电机控制芯片的时钟缓冲
Modelling: The clock buffer of a motor-control chip
步骤 Step | 内容 What we do
① 问题 Problem | 电机控制芯片的时钟经缓冲器分发到 PWM 计数器。缓冲器上升、下降延时不同，时钟占空比就会走样。尺寸比怎样取才能让两种延时接近？ The motor-control chip distributes its clock through buffers to the PWM counter. Unequal rise and fall delays distort the duty cycle. Which size ratio matches them?
② 建模 Model | 一阶 RC 模型；负载 = 4 × 输入电容 + 自载；忽略输入边沿斜率 First-order RC model; load = 4 × input capacitance + self-load; input slope ignored
③ 求解 Solve | Wp/Wn = 1：tPHL ≈ 29、tPLH ≈ 64 ps（差 77%）；Wp/Wn = 2.25：两者 ≈ 47 ps；Wp/Wn ≈ 1.50：tp ≈ 45 ps 最小 Wp/Wn = 1: tPHL ≈ 29, tPLH ≈ 64 ps (77% apart); Wp/Wn = 2.25: both ≈ 47 ps; Wp/Wn ≈ 1.50: smallest tp ≈ 45 ps
④ 检验 Check | 虚拟实验 1.3：FO4 下扫描尺寸比，读波形和下方延时曲线 Lab 1.3: sweep the ratio at FO4, read the waveform and the delay plot
⑤ 修正 Improve | 时钟缓冲选对称尺寸；普通逻辑取 √r 附近省面积；实际还要考虑输入斜率和工艺角 Use symmetric sizing for clock buffers and about √r for ordinary logic; real designs also account for input slope and corners
生活中的例子
Everyday example
跷跷板两边体重不同，要挪支点才能平衡
On a seesaw with unequal weights, move the pivot to balance it
芯片设计也靠模型：先用简单模型估算，再用仿真和工艺库校准，最后指出模型的局限。
Chip design runs on models: estimate simply, calibrate with simulation and the process library, then name the limits.
Notes: 对照五步讲解，强调第⑤步：模型在哪里失效。实验报告第六部分按这五步写。数值为示意参数下的结果，以后按 SKY130 校准。 Walk through the five steps, stressing step ⑤. Section 6 of the lab report follows them. Numbers use illustrative parameters, to be calibrated to SKY130.

## Slide 18
1.4 机器人问题 Robot problem
驱动板上的栅极驱动器
Driving the gate driver on the board
芯片的 PWM 输出要经焊盘、走线驱动电路板上的栅极驱动器输入，总负载约 10 pF。最小反相器直接驱动要几十纳秒，PWM 边沿被拖慢。插几级缓冲最快？
The chip’s PWM output drives pad, trace and gate-driver input, about 10 pF in all. A minimum inverter takes tens of nanoseconds, smearing the PWM edges. How many buffer stages are fastest?
已知 Given
负载 CL = 10 pF
load CL = 10 pF
第一级输入电容 Cin ≈ 2.46 fF
first-stage Cin ≈ 2.46 fF
边沿延时要求 < 0.3 ns
edge delay must be < 0.3 ns
本节结束时，我们用建立的模型回答这个问题。 We will answer it with this lesson’s model at the end.
Notes: 先让学生估一估、讨论 2 分钟，不急于给答案。本节最后回到这一页。 Let students estimate and discuss for two minutes; return to this problem at the end.

## Slide 19
1.4 概念 Concept
反相器链：逐级放大
Inverter chain: grow stage by stage
总扇出 F = CL / Cin，N 级等比链每级扇出 f = F^(1/N)
Total fan-out F = CL / Cin; each of N stages has f = F^(1/N)
总延时 t = N · tp0 · (γ + f)，γ 为自载与输入电容之比
Total delay t = N · tp0 · (γ + f), γ = self-load / input capacitance
最优 f 满足 f(ln f − 1) = γ：γ = 0 时 e ≈ 2.7；工程上常取 4，本模型 γ ≈ 0.67，最优 f ≈ 3.3
The optimum satisfies f(ln f − 1) = γ: e ≈ 2.7 for γ = 0; engineers often use 4; here γ ≈ 0.67 gives f ≈ 3.3
级数奇偶决定输出是否反相
An odd or even number of stages decides whether the output is inverted
经验公式 N ≈ ln F / ln 4 最优 f(ln f − 1) = γ
Rule of thumb N ≈ ln F / ln 4 optimum f(ln f − 1) = γ
Notes: 讲清公式中每个量的意义和模型的适用条件，再进入动画。 Explain each quantity and the model’s conditions before the animation.

## Slide 20
1.4 动画 Animation
一级驱动和六级驱动，延时为什么能差一百多倍？
Why can one stage and six stages differ in delay by more than a hundred times?
点击画面播放 · 中英字幕 · Click to play · bilingual captions
Notes: 播放动画，在关键画面暂停提问。 Play the clip and pause at the key frame to ask the question on the slide.

## Slide 21
1.4 虚拟实验 Virtual lab
动手试一试：传播延时与反相器链
Try it: Propagation delay and the inverter chain
任务 Tasks
CL = 10 pF：找出延时真正最小的级数（与 ln F / ln 4 比较）
CL = 10 pF: find the truly fastest N (compare with ln F / ln 4)
6 级时每级扇出 f 是多少？
What is f with 6 stages?
延时 < 0.3 ns 的最少级数
Fewest stages for a delay under 0.3 ns
打开虚拟实验 Open lab ▶
实验台中选“1.4”选项卡 · 课后按实验指导书完成实验报告
Choose tab 1.4 · write the lab report using the lab guide
Notes: 课堂投屏演示机器人任务，其余任务课后完成，并按实验指导书写实验报告。 Demonstrate the robot task in class; students finish the rest and the lab report after class.

## Slide 22
1.4 回到实际问题 Back to the problem
建模求解：驱动板上的栅极驱动器
Modelling: Driving the gate driver on the board
步骤 Step | 内容 What we do
① 问题 Problem | 芯片的 PWM 输出要经焊盘、走线驱动电路板上的栅极驱动器输入，总负载约 10 pF。最小反相器直接驱动要几十纳秒，PWM 边沿被拖慢。插几级缓冲最快？ The chip’s PWM output drives pad, trace and gate-driver input, about 10 pF in all. A minimum inverter takes tens of nanoseconds, smearing the PWM edges. How many buffer stages are fastest?
② 建模 Model | 等比反相器链，第一级为最小对称反相器；负载集中为 10 pF；每级 RC 模型 Tapered chain starting from a minimum symmetric inverter; 10 pF lumped load; RC model per stage
③ 求解 Solve | F ≈ 4070，ln F / ln 4 ≈ 6.00；单级 ≈ 41 ns；6 级 f ≈ 4.0、t ≈ 279 ps；真正最快为 7 级（f ≈ 3.3，275 ps），只快 1%；5 级 296 ps 即满足 < 0.3 ns F ≈ 4070, ln F / ln 4 ≈ 6.00; one stage ≈ 41 ns; 6 stages f ≈ 4.0, t ≈ 279 ps; truly fastest is 7 stages (f ≈ 3.3, 275 ps), only 1% better; 5 stages (296 ps) already meet < 0.3 ns
④ 检验 Check | 虚拟实验 1.4：CL = 10 pF，级数 1–10 扫描，对照 0.3 ns 线 Lab 1.4: CL = 10 pF, sweep 1–10 stages against the 0.3 ns line
⑤ 修正 Improve | 最优附近曲线很平：可少用一级省面积和功耗；要同相输出取偶数级；焊盘和走线电感还会带来振铃 The optimum is flat: drop a stage to save area and power; use an even count for a non-inverted output; pad and trace inductance add ringing
生活中的例子
Everyday example
搬重物接力：一人搬太慢，分几段逐级加人更快，但人太多交接也费时
Relay carrying: one person is slow, adding people stage by stage is faster, but too many hand-offs waste time
芯片设计也靠模型：先用简单模型估算，再用仿真和工艺库校准，最后指出模型的局限。
Chip design runs on models: estimate simply, calibrate with simulation and the process library, then name the limits.
Notes: 对照五步讲解，强调第⑤步：模型在哪里失效。实验报告第六部分按这五步写。数值为示意参数下的结果，以后按 SKY130 校准。 Walk through the five steps, stressing step ⑤. Section 6 of the lab report follows them. Numbers use illustrative parameters, to be calibrated to SKY130.

## Slide 23
1.5 机器人问题 Robot problem
巡线小车控制芯片的功耗预算
Power budget of a line-following car controller
巡线小车的控制芯片约 1 万个门，平均每个时钟有 10% 的门发生 0→1 翻转，时钟 100 MHz。动态功耗多大？把电压从 1.8 V 降到 1.2 V 能省多少，又要付出什么代价？
The line-following car’s controller has about 10 000 gates, 10% making a 0→1 transition each cycle at 100 MHz. What is the dynamic power? How much does dropping from 1.8 V to 1.2 V save, and at what cost?
已知 Given
门数 N = 10 000，0→1 翻转率 α = 0.1
N = 10 000 gates, 0→1 activity α = 0.1
时钟 f = 100 MHz
clock f = 100 MHz
每门负载 C = 5 fF
load per gate C = 5 fF
本节结束时，我们用建立的模型回答这个问题。 We will answer it with this lesson’s model at the end.
Notes: 先让学生估一估、讨论 2 分钟，不急于给答案。本节最后回到这一页。 Let students estimate and discuss for two minutes; return to this problem at the end.

## Slide 24
1.5 概念 Concept
动态功耗：每次翻转的能量
Dynamic power: the energy per transition
0→1：电源送出 CV²，一半存进电容，一半在 PMOS 上变成热
0→1: the supply delivers CV², half stored, half burnt in the PMOS
1→0：电容里的 ½CV² 在 NMOS 上变成热
1→0: the stored ½CV² is burnt in the NMOS
动态功耗与电压平方成正比
Dynamic power scales with the square of the supply
降压使电流变小、门变慢：tp ∝ VDD / (VDD − VT)²
Lower supply means less current and slower gates: tp ∝ VDD / (VDD − VT)²
P = α · C · VDD² · f · N （α：每个时钟 0→1 翻转的概率）
α = probability of a 0→1 transition per cycle
Notes: 讲清公式中每个量的意义和模型的适用条件，再进入动画。 Explain each quantity and the model’s conditions before the animation.

## Slide 25
1.5 动画 Animation
电容充一次电、放一次电，电源一共送出多少能量？都去哪里了？
One charge and one discharge: how much energy does the supply deliver, and where does it go?
点击画面播放 · 中英字幕 · Click to play · bilingual captions
Notes: 播放动画，在关键画面暂停提问。 Play the clip and pause at the key frame to ask the question on the slide.

## Slide 26
1.5 虚拟实验 Virtual lab
动手试一试：功耗
Try it: Power
任务 Tasks
读出默认设置下的动态功耗
Read the dynamic power at the default settings
电压降到 1.20 V，功耗降多少？
Lower the supply to 1.20 V: how much is saved?
FO4 ≤ 100 ps 的最低电压
Lowest supply with FO4 ≤ 100 ps
打开虚拟实验 Open lab ▶
实验台中选“1.5”选项卡 · 课后按实验指导书完成实验报告
Choose tab 1.5 · write the lab report using the lab guide
Notes: 课堂投屏演示机器人任务，其余任务课后完成，并按实验指导书写实验报告。 Demonstrate the robot task in class; students finish the rest and the lab report after class.

## Slide 27
1.5 回到实际问题 Back to the problem
建模求解：巡线小车控制芯片的功耗预算
Modelling: Power budget of a line-following car controller
步骤 Step | 内容 What we do
① 问题 Problem | 巡线小车的控制芯片约 1 万个门，平均每个时钟有 10% 的门发生 0→1 翻转，时钟 100 MHz。动态功耗多大？把电压从 1.8 V 降到 1.2 V 能省多少，又要付出什么代价？ The line-following car’s controller has about 10 000 gates, 10% making a 0→1 transition each cycle at 100 MHz. What is the dynamic power? How much does dropping from 1.8 V to 1.2 V save, and at what cost?
② 建模 Model | 只计动态功耗，不计漏电与短路电流；所有门负载相同；翻转率取平均值 Dynamic power only, no leakage or short-circuit current; identical gate loads; average activity
③ 求解 Solve | P = 0.1 × 5 fF × 1.8² × 100 MHz × 10⁴ = 1.62 mW；1.2 V 时 0.72 mW（降 56%）；FO4 ≤ 100 ps 要求 VDD 约 1.21 V（1.20 V 时 100.5 ps，刚好超标） P = 0.1 × 5 fF × 1.8² × 100 MHz × 10⁴ = 1.62 mW; at 1.2 V 0.72 mW (56% less); FO4 ≤ 100 ps needs about 1.21 V (100.5 ps at 1.20 V, just over)
④ 检验 Check | 虚拟实验 1.5：改电压、频率、翻转率，对照功耗曲线和 FO4 延时曲线 Lab 1.5: vary supply, clock and activity against the power and FO4 delay plots
⑤ 修正 Improve | 低电压、高温时漏电不能忽略；小车上电机耗电远大于芯片，芯片省电主要延长待机和传感器节点的电池寿命 Leakage matters at low voltage and high temperature; on the car the motors dominate, so chip savings mainly extend standby and sensor-node battery life
生活中的例子
Everyday example
手机省电模式：降频、降压，代价是变慢
Phone power-saving mode lowers clock and voltage, at the cost of speed
芯片设计也靠模型：先用简单模型估算，再用仿真和工艺库校准，最后指出模型的局限。
Chip design runs on models: estimate simply, calibrate with simulation and the process library, then name the limits.
Notes: 对照五步讲解，强调第⑤步：模型在哪里失效。实验报告第六部分按这五步写。数值为示意参数下的结果，以后按 SKY130 校准。 Walk through the five steps, stressing step ⑤. Section 6 of the lab report follows them. Numbers use illustrative parameters, to be calibrated to SKY130.

## Slide 28
例题 Worked example
对称反相器 Wn = 0.42 μm、Wp = 0.94 μm，驱动 4 个相同反相器（FO4）。求 tPHL。
A symmetric inverter, Wn = 0.42 μm and Wp = 0.94 μm, drives four identical inverters (FO4). Find tPHL.
IDSAT,n = ½k′n(W/L)(VDD − VT)² = 230 μA
IDSAT,n = ½k′n(W/L)(VDD − VT)² = 230 μA
Req,n ≈ ¾·VDD / IDSAT = 5.88 kΩ
Req,n ≈ ¾·VDD / IDSAT = 5.88 kΩ
Cin = (Wn + Wp)·Cg = 2.46 fF；自载 (Wn + Wp)·Cd = 1.64 fF
Cin = (Wn + Wp)·Cg = 2.46 fF; self-load (Wn + Wp)·Cd = 1.64 fF
CL = 4·Cin + 自载 = 11.47 fF；tPHL = 0.69·Req,n·CL ≈ 46.5 ps（虚拟实验 1.3 中验证）
CL = 4·Cin + self-load = 11.47 fF; tPHL = 0.69·Req,n·CL ≈ 46.5 ps (check it in lab 1.3)
Notes: 先让学生独立算 3 分钟，再展开；最后在虚拟实验 1.3 中设 Wp/Wn = 2.25、FO4 对照。 Give students three minutes, then work through it and check in lab 1.3 with Wp/Wn = 2.25 at FO4.

## Slide 29
本章小结
Chapter summary
互补结构：稳态无直流通路；导通管相当于电阻 Ron
Complementary structure: no static DC path; the on transistor acts as Ron
传输特性：VM 由两管强弱比决定，噪声容限保证抗干扰
Transfer curve: VM set by the strength ratio; noise margins give immunity
延时：tp = 0.69·Req·CL；Wp/Wn = r 对称，≈ √r 最快
Delay: tp = 0.69·Req·CL; Wp/Wn = r is symmetric, ≈ √r is fastest
大负载：等比反相器链，每级扇出约 3–4（经验取 4）
Large loads: a tapered chain with fan-out about 3–4 per stage (rule of thumb 4)
功耗：P = αCV²fN，降压最省电，但门会变慢
Power: P = αCV²fN; lowering VDD saves most, but slows the gates
课后：5 个虚拟实验任务 ＋ 实验报告（任选一个机器人问题）；预习第 2 章 组合逻辑门
After class: the five virtual labs + one lab report on a robot problem; preview Chapter 2, combinational gates
Notes: 回顾本章：一个反相器就包含了电平、速度、功耗三件事。后面的门电路、时序和版图都建立在这里。 Review: one inverter already contains levels, speed and power; the gates, timing and layout that follow build on this.